## Slide 1: Error codes
JS
Version: 2022/02/01

## Slide 2: 1. General 2. How to find the correct Error Code? 3. Main categories 4. Sub categories

## Slide 3: 1. General
Root document (where the Error Codes are defined/maintained):
FR_PRD_24_E_ErrorCodes.xlsx
These Error Codes were “copied” to:
  SQM (jitbit-sqmtool.televic.com)
  DQM (dqm.televic.com)
  Internal repair (S:\Quality\PQ04-Internal_repair, Excel file under TCS, THC and TRA)
  Label tool (template for printing “Non-Conform” labels)
And need to be maintained there “asynchronously” to keep synchronisation with FR_PRD_24.

## Slide 4: 2. How to find the correct Error Code?
What is the root cause of the failure?
=> Find the corresponding “Main category”
=> Find the specific “Sub category”
If you can cannot define a “Sub category”, use the “Main category”

## Slide 5: 3. Main categories
Main category | Main code
Component issue | 1000
Mechanical issue | 1100
Assembly issue | 1200
Part missing | 1300
SW/FW issue | 1400
Documentation issue | 1500
Logistic issue | 1600
Label issue | 1700
Oxidation, Humidity & Liquid | 1800
Contamination | 1900
Version error | 2000
Test system issue | 3000
Replaced out of precaution | 8000
Retrofit on TLV demand | 8100
Customer issue | 9000
Retrofit on Client demand | 9100
Costs too high | 9900
These are typically reported during Incoming Inspection.

## Slide 6: 4. Sub categories
In blue, the ones that are typically reported by Incoming Inspection.

## Slide 7: 1000 - Component issue
Component burnt out / blown up | 1001 | 
Component defect | 1002 | 
Component fysically broken | 1003 | E.g. broken connector due to bad packaging
Component out of spec | 1004 | 
Component worn out | 1005 | 
PCB fault | 1020 | PCB = Bareboard (without population)!
PCB fault – Short circuit | 1021 | 
PCB fault – Open | 1022 | 
PCB fault – Via problem | 1023 | 
Module defect | 1030 | E.g. defect power supply module of the product
Module wrong type | 1031 | 
Module burnt out | 1032 | 
With component we define a “catalog” part which we purchase from an external party
which is not a subcontractor (Televic Bulgaria, KAT, Proplace,..).
E.g. a connector, chip, power module, camera, display,..

## Slide 8: 1100 - Mechanical issue
Wrong screening | 1180 | 
Dimension / Tolerances - Not OK | 1181 | Typically noticed after measurement via QI09
Flatness not OK | 1182 | Check required by QG09 for MECH
Sharp edges | 1183 | Check required by QG09 for MECH
Aspect / Finish / Surface - Not OK | 1190 | See WI_QA_04_E-VisualInspectionStandardMechanicalParts
= Applicable to delivery of mechanical parts
(which can already be assembled in a product by a subcontractor),
that are based on a drawing/specification from Televic.
Therefore, mechanical parts should not be confused with “components” (see before).

## Slide 9: 1200 - Assembly issue
Mounting error | 1201 | E.g. wrong sequence washer, spring washer and nut
Bad contact | 1202 | 
Jumpers wrong setting | 1203 | Typically defined in E07
Not tested when test is required | 1204 | See E15 (TRA), E09
Damaged by operator | 1205 | 
Component wrong type | 1206 | E.g. wrong component value populated (other resistor/capacitor value,..)
Soldering failure | 1210 | 
Soldering failure – Open | 1211 | E.g. cold solder joint
Soldering failure – Short | 1212 | 
Soldering failure – Missing | 1213 | E.g. one of the PTH lead-outs not soldered
Component polarisation | 1214 | 
Component - Incorrect placement | 1215 | E.g. not placed acc. to IPC-A-610x
Component - Lifted / Tombstoning | 1216 | 
Component - Leads too long | 1217 | E.g. lead-outs longer than 2,5mm (see IPC-A-610H section 7.3)
Component - Silicon | 1218 | E.g. missing silicon around ELCO’s (typically specified in E07)
Wiring fault | 1220 | E.g. contacts not well crimped (acc. to IPC WHMA-A-620x), or incorrect wire-wrap
Conformal coating (tropicalisation) | 1230 | E.g. coating on connector contacts
Loose component / not tightened | 1240 | E.g. screw not tightened acc. to required torque (E07 or WI_PRD_15_E_Torques)
= Typically noticed on units assembled internally or by subcontractors
(Televic Bulgaria, KAT, Proplace,..)

## Slide 10: 1300 - Part missing
No sub categories
E.g.:
Jumper not placed
Parts that need to be delivered separately missing
..

## Slide 11: 1400 - SW/FW issue
Program fault | 1410 | 
Update | 1420 | 

## Slide 12: 1500 - Documentation issue
Work instruction | 1501 | E.g. E07, E15,.. incorrect or incomplete
=> Typically such NCR’s will not have the tag “Complaint” (and will not be sent to the supplier),
But will have the tag “Televic internal” so that they are followed-up internally.

## Slide 13: 1600 - Logistic issue
Wrong delivery | 1610 | E.g. Manufacturer Part Number (MPN) “BC547B” ordered, “BC557B” delivered
Wrong quantity | 1611 | 
Internal transport | 1620 | 
External transport | 1630 | E.g. boxes damaged during SEA/AIR shipment (by forwarder). Should be checked by Goods Receipt during “Acceptance from carrier” process..
Packaging not correct/sufficient | 1640 | 

## Slide 14: 1700 - Label issue
Label missing | 1710 | 
E.g. label on wrong position: Take main category (1700 – Label issue)

## Slide 15: 1800 - Oxidation, Humidity & Liquid
Water ingress | 1801 | 
Liquid damage | 1802 | 
Oxidation | 1803 | 

## Slide 16: 1900 Contamination
Foreign objects | 1901 | E.g. screw “loose” in housing

## Slide 17: 2000 - Version error
No sub categories
E.g. RevLev (BOM) 1.03 ordered and RevLev (BOM) 1.02 delivered.

## Slide 18: 3000 - Test system error
False reject | 3001 | 

## Slide 19: 8000 - Replaced out of precaution
No sub categories

## Slide 20: 8100 - Retrofit on TLV demand
No sub categories
E.g. when R&D decides to revise (via an ECN) the part/product, e.g. to add a new feature.
The parts/products can be returned to the supplier via a ticket “Request for Rework” and above Error code.

## Slide 21: 9000 - Customer issue
No failure found | 9001 | 
Vandalism/Misuse/Abuse | 9002 | 
Not made by Televic = Not delivered by Televic | 9003 | The failing material the customer has returned under RMA was not sold/delivered by Televic (another supplier sold/delivered this material to the customer). Note; don’t confuse with 3rd party materials which we buy & sell directly to the customer.
Damaged | 9004 | 

## Slide 22: 9100 - Retrofit on Client demand
Overhaul / Maintenance | 9101 | For TRA, some products are returned for regular maintance & preventive replacement of parts.

## Slide 23: 9900 - Costs too high
Damaged beyond repair | 9901 | No further investigation for the root cause will be done, as the cost for investigation >> the cost for repair.
Sealed product | 9902 | E.g. customer returns materials (for credit) which are still well sealed (typically THC products), and can be put back into stock without verification.
Refused - In conflict with RMA procedure | 9903 | Refused: E.g. customer returns materials (for credit) saying they were “not used”, however upon receival & inspection, we notice the customer actually did use these materials.
No standard product (special production) | 9904 | 
Fault Unknown | 9999 |